## Slide 1: EPA’s Label Review Manual Update Chapter 10: Worker Protection Labeling
February 7, 2013
Richard Pont
Certification and Worker Protection Branch
Office of Pesticide Programs

## Slide 2: Overview
What is the Label Review Manual (LRM)?
Overview of LRM Review Process
Overview of LRM Chapter 10
Key Revisions Planned
Intended Outcomes

## Slide 3
What is the LRM?

## Slide 4: LRM Review Process
Began in 2010
LRM Chapters posted on EPA’s web site for review and comment at regular intervals
14 0f 18 LRM chapters updated and posted as of today
Expect to be completed by 2013
http://www.epa.gov/oppfead1/labeling/lrm/

## Slide 5: LRM Review Process
The LRM review process does NOT establish new guidance or regulatory/labeling policy; it is intended to compile, clarify, and reiterate existing Agency policies and interpretations of statutory or regulatory provisions.

## Slide 6: Overview of LRM Chapter 10
Worker Protection Labeling
  Worker Protection Standard (WPS) background
  Determining WPS scope
  WPS label statements
  Precautionary statements
  Directions for use
  Determining Restricted Entry Intervals (REIs)
  Labeling statements for special situations

## Slide 7: Overview of LRM Chapter 10
Precautionary statements:
  There are four types of worker protection statements that generally appear in the precautionary statements of a label. They are as follows:
Handler Personal Protective Equipment (PPE)
Statements for Contaminated PPE
Engineering Controls
User Safety Recommendations

## Slide 8: Key Revisions Planned
Handler Personal Protective Equipment: Glove Statements
  Clarify directions for dry and water-based formulations (i.e., WATERPROOF gloves)
  Specify ALL acceptable glove types for product, and order by cost
  Provide glove options for “short duration” handler tasks

## Slide 9: EPA Chemical Resistance Category Selection Chart for Gloves
Solvent Category | Barrier Laminate | Butyl Rubber ≥ 14 mils | Nitrile Rubber ≥ 14 mils | Neoprene ≥ 14 mils | Nitrile Rubber ≥ 14 mils* | Poly-ethylene | Polyvinyl Chloride (PVC) ≥ 14 mils | Viton ≥ 14 mils
A (dry and water based) | High | High | High | High | High | High | High | High
B | High | High | Slight | Slight | None | Slight | Slight | Slight
C | High | High | High | High | Moderate | Moderate | High | High
D | High | High | Moderate | Moderate | None | None | None | Slight
E | High | Slight | High | High | Slight | None | Moderate | High
F | High | High | High | Moderate | Slight | None | Slight | High
G | High | Slight | Slight | Slight | None | None | None | High
H | High | Slight | Slight | Slight | None | None | None | High

## Slide 10: Key Revisions Planned
Handler Personal Protective Equipment: Respiratory Protection Requirements
  Clarify labeling language for respiratory protection requirements
  Address EPA inconsistencies with NIOSH respirator terminology

## Slide 11: Intended Outcomes
Provide better guidance for OPP product managers/reviewers, registrants, and state registration specialists
Provide better standard “boilerplate” label language and precautionary statements
Improve quality and consistency of pesticide product labels
Provide better flexibility and cost effective options for end users while still ensuring protection

## Slide 12
Questions?