## Slide 1: UN Performance Packaging Standards
Chris Lind
Director Technology & Regulatory Affairs
Mauser USA LLC

## Slide 2: Quick History
Packagings used to be specification based—the government told us packing manufacturers what the drums, etc. should look like and how they should be constructed
In the 1990s the US DOT harmonized with the UN Model Regulations and went to Performance Oriented Packaging (POP), meaning they had to have specific performance attributes

## Slide 3: UN Subcommittee of Experts on the Transport of Dangerous Goods
29 voting countries
5 Non-voting observer countries
35 Non-Governmental Organizations, Consultative Organizations etc.
  5 are international packaging groups (ICPP, ICIBCA, ICCR, ICDM, & IFDI)
  Chemicals are represented by CEFIC and ICCA
Non-voting participants can present both INFormal papers and Working Papers for consideration by the voting members and participate in discussion

## Slide 4: UN Model Regulations & US DOT Regulations
Define what is a design and require Design Qualification tests on all new designs, including remanufactured IBCs
Requirements for recertification of design
  USA—yearly
  Canada—every other year
  Europe—none. Once a DQ is certified they’re done

## Slide 5: Regulations Establish Hazard Classes & Packing Groups
Hazard Classes
Explosive
Compressed gas
Flammable liquid
Flammable Solid
Oxidizer
Poison/Infectious Substance
Radioactive
Corrosive
Miscellaneous
Packing Groups
PG I Extreme Hazard
PGII Major Hazard
PGIII Minor Hazard

## Slide 6: Regulations Establish Testing Procedures
Vibration test– one hour vibration at 1.6 mm lift
Bottom Lift – Two lifts each way with 1.25 x permissible mass
Stack Tests – 24 hour
Leak Proofness – 5 minutes at 20 kPa PG II & PG III
  Every bottle in production must be leak tested at 20 kPa for PG II & PG III
Hydrostatic Pressure – IBCs require 10 minutes at 100 kPa in EU; can be less in US & Canada
Drop Test– 0.67-1.2 meters with IBC at -18°C for PG III compliance

## Slide 7: Other DOT Regulatory Requirements
Training
Quality System
Security Training
Security Plan
Load Securement
  All modal regulations require that the load be secured from movement in every direction

## Slide 8: 31HA1/Y/mm-yr/USA/M#/3800/2038/1041/57/100/mm-yr mm-yr/
UN Symbol
CODE (49 CFR 178.702(a))
  Referenced in law as 31HZ1
Packing Group Y or Z. (X (PG I) not allowed by law in 31HZ1 IBC)
Month and Year of manufacture
Country authorizing mark
Manufacturer # or 3rd Party Lab# or other registered symbol
Stacking load in kg
Maximum permissible gross mass in kg
Rated capacity in L at 20 degrees C
Tare mass
Gauge test pressure in kPa
Date of last leakproofness test
Date of last inspection
Bottle must have code, M#, date of manufacture and country authorizing mark
Finished unit also must have sticker with maximum allowable top load in transit 31HA1/31HG1/M4118/06 09/USA

## Slide 9: What makes an IBC meet the RPCL?
Packing Group III compliance
  Y or Z on the UN Mark
  Meets the testing requirements for PGIII
Tamper Evidence
  Valve handle
  Foil Seal on valve
  Cap
One way or check valve
  There are no requirements at this time regarding how much back pressure this check should handle.
Unique Serial Number or other traceability system/device
There is no such thing as a UN rated single use or one-way IBC. To reuse/refill or not is the choice of the user, not the government, as long as it meets the legal requirements.

## Slide 10: Refill versus New IBCs
The totals of the 2011 numbers received are the following: New Composite IBCs (all sizes combined) 2,574,513 New IBC Bottles (all sizes combined) 860,296 The totals of the 2010 numbers received are the following: New Composite IBCs (all sizes combined) 2,107,425 New IBC Bottles (all sizes combined) 650,484
Reconditioned, Repaired and Remanufactured units not included as one IBC can make several trips per year.

## Slide 11: Rigid Bulk Packaging Demand by Market
11

## Slide 12
Market studies lump all agricultural products together
Does not include demand for reconditioned, repaired or remanufactured units
Does not reflect manufacturers’ market concentrations
  Some vendors are heavier into ag chemicals than others
  Does not reflect composite IBCs versus “asset tanks” or metal IBCs
Reporting may not be as accurate as one might think
  These studies are supposed to be blind—but do reporting entities over or under report
Bottom line is that despite inherent inaccuracies a substantial number of IBCs are sold for pesticides and are refilled many times

## Slide 13: Thank You